## Slide 1: Trickle ICE
Incremental Provisioning of Candidates for the Interactive Connectivity Establishment (ICE) Protocol
draft-rescorla-mmusic-ice-trickle
Eric Rescorla
Justin Uberti
Emil Ivov

## Slide 2: Why
Simply stated: makes call setup faster
  Don't need to wait for all candidates/servers to respond
  Encourages use of multiple STUN/TURN servers
  Savings occurs on both sides
  Removes need for magic timeouts
In a typical app, call setup is improved by 500+ ms in:
25% of calls (globally)
50% of calls (developing markets)
Even more if service is not multi-datacenter

## Slide 3: The Problem
Alice’s NAT
Bob’s NAT
STUN Server
STUN Server
Bob
Alice
Vanilla ICE Operation as per RFC 5245
discovery
offer and candidates
… connectivity checks …
answer and candidates
discovery

## Slide 4: The Solution send candidates as you get them
Alice’s NAT
Bob’s NAT
STUN Server
STUN Server
Bob
Alice
Trickle ICE
discovery
discovery
offer and ICE description (and host candidates)
answer and ICE description (and host candidates)
… more candidates and connectivity checks …

## Slide 5: Current state
Trickle ICE is already implemented in existing signaling protocols and real-world apps
  XMPP (XEP-0176), JSEP (Chrome)
  Google Talk, Empathy, etc
But we need to nail down the exact interactions with RFC 5245
  draft-rescorla-mmusic-ice-trickle does this

## Slide 6: Relationship to SIP, Offer/Answer and SDP
Extends existing ICE Offer/Answer Model
  Defines semantics for Trickle ICE
  ICE credentials are exchanged via offer/answer
  More ICE candidates can be sent after credentials
Defines SDP for negotiating Trickle ICE
Outer signaling is left abstract
  No SIP message for candidates defined by this specification

## Slide 7: Details for Trickle ICE
How to send additional candidates, and indicate that all candidates have been gathered
How to handle ICE check list states when trickling
How to keep checks synchronized from both ends (since we can no longer rely on stream and pair ordering)

## Slide 8: end-of-candidates
Bob
Alice
Delivers All Candidates
Connectivity Checks Fail
end-of-candidates
Delivers Some Candidates
Delivers Additional Candidates
New Connectivity Checks Succeed

## Slide 9: Backwards Compatibility
A non-Trickle callee can't handle a Trickle offer
Full Trickle
  If you know remote side supports Trickle ICE (via XMPP Disco, Cap Neg, or other out-of-band mechanism)
  Both caller and callee can trickle
Half Trickle
  Caller cannot trickle, but answerer can
  Still get half the latency savings

## Slide 10: SDP Details
Need SDP to indicate Trickle support
  a=ice-options:trickle
Need way to generate valid SDP with no candidates
  For cases where we don’t want to send host candidates for privacy reasons
  C=0.1.2.3
  M=9999
  A=candidate:0.1.2.3