## Slide 1: Trickle ICE
Incremental Provisioning of Candidates for the Interactive Connectivity Establishment (ICE) Protocol
draft-rescorla-mmusic-ice-trickle
Eric Rescorla
Justin Uberti
Emil Ivov

## Slide 2: Intro
Why
  Numbers (justin)
  Call setup is delayed by this much
  Removes magic timeouts
  Discourages using multiple STUN/TURN servers
  Not always addressable via pre-call gathering

## Slide 3: The Problem
Alice’s NAT
Bob’s NAT
STUN Server
STUN Server
Bob
Alice
Vanilla ICE Operation as per RFC 5245
discovery
offer and candidates
… connectivity checks …
answer and candidates
discovery

## Slide 4: The Solution send candidates as you get them
Alice’s NAT
Bob’s NAT
STUN Server
STUN Server
Bob
Alice
Trickle ICE
discovery
discovery
offer and ICE description (and host candidates)
answer and ICE description (and host candidates)
… more candidates and connectivity checks …

## Slide 5: Other protocols
Trickle is already implemented in signaling protocols
  XMPP (XEP-0176)
  WebRTC (Chrome)
Used in real-world applications
  Google Talk etc
But we need to nail down the exact interaction with RFC 5245

## Slide 6: What’s missing in RFC5245 Why is trickling not currently compatible
We need to know how long to wait for additional candidates (an end-of-candidates message)
We need to know exactly how to update check list states
We need to keep checks synchronized from both ends (since we can no longer rely on stream and pair ordering)
Even if we deliver them additional candidates are likely to be ignored or cause problems with Vanilla ICE implementations
  Lack of host candidates in an offer/answer would probably result in a failure
  Premature failures in cases where lack of connectivity for the first set of candidates can be easily determined
Resolve SDP-specific Issues.

## Slide 7: end-of-candidates
Bob
Alice
Delivers All Candidates
Connectivity Checks Fail
end-of-candidates
Delivers Some Candidates
Delivers Additional Candidates
New Connectivity Checks Succeed

## Slide 8: Relationship to SIP, Offer/Answer and SDP
Uses Offer/Answer Model
  ICE credentials are exchanged via offer/answer
  ICE candidates can be sent after credentials
Signaling is left abstract
  No SIP message for candidates defined by this specification

## Slide 9: Backwards Compatibility
If you know remote side supports Trickle
  Via XMPP Disco, Cap Neg, or other out-of-band mechanism
  Offerer can trickle
If not
  Offerer cannot trickle, but answerer can
  Still get half the latency savings

## Slide 10: SDP Details
Need SDP to indicate Trickle support
  a=ice-options:trickle
Need way to generate valid SDP with no candidates
  For cases where we don’t want to send host candidates for privacy reasons
  C=0.1.2.3
  M=9999
  A=candidate:0.1.2.3