## Slide 1: Trickle ICE
Incremental Provisioning of Candidates for the Interactive Connectivity Establishment (ICE) Protocol
draft-ivov-mmusic-trickle-ice
Eric Rescorla
Justin Uberti
Emil Ivov

## Slide 2: Reminder: Vanilla ICE
STUN Server
STUN Server
Bob
Alice
Vanilla ICE as per RFC 5245
disco
disco
offer and candidates
… connectivity checks …
answer and candidates

## Slide 3: Reminder: Vanilla ICE vs Trickle ICE
STUN Server
STUN Server
Bob
Alice
Vanilla ICE as per RFC 5245
disco
disco
offer and candidates
… connectivity checks …
answer and candidates
STUN Server
STUN Server
Bob
Alice
disco
disco
O/A with host or no cands
… more cands & conn checks …
Trickle ICE

## Slide 4: Reminder: Starting Checks
Maintains Active/Frozen checklist state
  (rather than deducing it)
Start checks as soon as we have one non-empty list
Unfreeze the other check lists once the first one completes
  (Inherited from 5245 but might be worth updating to: “unfreeze as soon as non-empty”)

## Slide 5: Reminder: Ending Checks
Vanilla ICE: Every time a conn check completes thou shalt update states and fail a check list if:
  all of its pairs are either in the Failed or Succeeded state;
  at least one of the components of the media stream has no pairs in its valid list.
Trickle ICE adds the following conditions:
  all candidate harvesters have completed and the agent is not expecting to learn any new candidates;
  the remote agent has sent an end-of-candidates indication for that check list

## Slide 6: TODOs from Last Time
Clarify relationship with Offer/Answer
Define SDP for Offers and Answers
Define SDP for trickled candidates
Expand on half-trickle
Provide a SIP usage
What about ICE Lite …

## Slide 7: Changes to the SDP
Advertising support for trickle ICE:
  a=ice-options:trickle
Offers and answers with no candidates:
  c=IN IP4 0.0.0.0
  m=audio 1 RTP/AVP 0 96
New candidates and end of candidates
  …
  a=candidate:1 1 UDP 1234 1.2.1.4 5000 typ host
  a=candidate:2 1 UDP 5678 6.1.2.3 5000 typ srflx
  a=end-of-candidates

## Slide 8: Support and Discovery
Removed requirements for pre-verifying support
Draft now mandates use of half trickle when pre-verifying is impossible (important for SIP):
  Offerer starts as with vanilla 5245 ICE
  Answerer sees a=ice-options:trickle and trickles
  All subsequent Offers/Answers can use trickle

## Slide 9: Half Trickle
STUN/TURN Server
Bob
STUN /TURN Server
Alice
disco
disco
Offer with all candidates
Answer with no candiates
… more cands & conn checks …
Enjoying FULL TRICKLE from then on

## Slide 10: Open Issues MID vs Stream Index
Do we really need the stream index option?
Possible application syntax (do we want to spec this)?
For example:
a=mid:1
a=candidate:1 1 UDP 16582 12.18.10.3 5000 typ host
a=candidate:2 1 UDP 16584 96.1.2.3 5000 typ srflx
a=end-of-candidates
a=mid:2
a=candidate:2 1 UDP 16915 96.1.2.3 5002 typ srflx

## Slide 11: Open Issues Session or media level end-of-candidates
c=IN IP4 12.18.10.3
a=end-of-candidates
m=audio 5000 RTP/AVP 0 96
a=candidate:1 1 UDP 16582 12.18.10.3 5000 typ host
m=video 5000 RTP/AVP 0 96
a=candidate:2 1 UDP 16915 96.1.2.3 5002 typ srflx
VS
(our preference)
c=IN IP4 12.18.10.3
m=audio 5000 RTP/AVP 0 96
a=candidate:1 1 UDP 16582 12.18.10.3 5000 typ host
a=end-of-candidates
m=video 5000 RTP/AVP 0 96
a=candidate:2 1 UDP 16915 96.1.2.3 5002 typ srflx
a=end-of-candidates

## Slide 12: Open Issues ICE Lite and Candidate Signalling (Christer)
Trickle ICE Lite agents can learn all their peers’ addresses as peer reflexive.
Should we have the option of not sending them through signalling as well
ICE Lite Server
STUN /TURN Server
Alice
XXX
disco
Answer with no cands a=ice-lite
Offer with no cands
Conn Checks
NO MORE SIGNALLING

## Slide 13: Open Issues New Candidates after ICE Completion? (Mobility)
Option 1: Require ICE Restart (harmless really)
Option 2: Process (How? Why?)
STUN /TURN Server
Alice
How do I tell Bob about my new srflx addr?
Trickle vs Restart
eth0
eth1 comes up
Alice
media
media

## Slide 14: Appendix: A SIP Usage for Trickle ICE (1/3)
SIP Applications would always do half trickle unless explicitly configured otherwise
Trickling will happen with in-dialog SIP INFO requests as per RFC 6086
The INFO Package token name for this package is "trickle-ice”
  Does not mandate GRUU support
Does not remove the requirement for doing a re-INVITE upon completion of ICE processing.

## Slide 15: Appendix: A SIP Usage for Trickle ICE (2/3)
INFO sip:alice@example.com SIP/2.0
...
Info-Package: trickle-ice
Content-type: ?application/sdp? <- … ahem
Content-Disposition: Info-Package
Content-length: ...
a=mid:1
a=candidate:1 1 UDP 1658497328 192.168.100.33 5000 typ host
a=candidate:2 1 UDP 1658497328 96.1.2.3 5000 typ srflx
a=mid:2
a=candidate:2 1 UDP 1658497328 96.1.2.3 5002 typ srflx
a=end-of-candidates

## Slide 16: Appendix: A SIP Usage for Trickle ICE (3/3)
STUN/TURN Server
Bob
STUN /TURN Server
Alice
disco
disco
5245 SIP re-INVITE
200 OK
INVITE (Offer)
180 (Answer)
INFO (More Cands)
more cands & conn checks
200 OK
media